## Slide 1
Top-down introduction to Networking
(through example)
Lecture
2
Topic 1: Foundation
Webserver
Client Request
Server Reply
Browser
Notes: Image source: http://putitlive.com/img/webserver.png

## Slide 2
  Recap: OSI and Internet Architecture
  Application example
  (Browser fetching HTTP document from webserver)
Today’s lecture outline

## Slide 3
OSI
Architecture
Notes: OSI architecture:
ISO was one of the first organizations to formally define a common standard way to connect computers.
Their architecture called Open Systems Interconnection architecture partitioned network functionality into seven layers where one or more protocols implement the functionality assigned to a given layer. In this sense, OSI model is not a protocol graph (since it defines layers and not relationships between protocols) but a reference model.
ISO, in conjunction with another standardization body called ITU, publishes a series of protocol specifications based on the OSI model. This series is sometimes called the X dot series since the protocols are given names like X.25, X.400 and X.500.
Starting at the bottom and moving up, the physical layer handles the transmission of raw bits over a communications link. The data link layer then collects a stream of bits into a large aggregate called a frame. Network adapters, along with device drivers, running in the node's OS typically implement this layer. This means that frames (and not raw bits) are delivered to hosts. The network layer handles routing among nodes within a packet switched network. At this layer, the unit of data exchange is a packet rather than a frame, although they are fundamentally the same thing. The lower three layers are implemented on all nodes nodes in cluding switches within the netwok and hosts connected along the exterior of the network. The transport layer then implements what we have up to this point being called the process to process channel. Here the unit of data is called a message (or segment) rather than a packet or a frame. The transport layer and the higher layers typically run only on the end hosts and not on the intermediata switches or routers.
There is less agreement about the definition of the top layers. Skipping ahead to the seventh layer (the top most layer), we find the application layer. Example protocols include HTTP and FTP. Below that presentation layer is concerned with the format of data exchanged between peers; e.g., whether an integer is 16/32/64 bits long and whether the MSB is trasmitted first or last. Finally, the session layer provides a name space that is used to tie together potentially different transport streams that are part of a single application. For example, an audio stream and a video stream may be managed in a teleconferening application.

## Slide 4
Internet Architecture
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Narrow Waist
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
Notes: Internet Architecture:
The internet architecture, also called TCP/ IP architecture based on its two most famous protocols. is shown above. The architecture evolved from experience in implementing ARPANET.
While the 7 layer OSI model can be applied to the Internet (with some imagination), a four layer model is used instead. At the lowest layer is a variety of network protocols (also called data link layer or subnetwork layer). In practice, these protocols are implemented using a combination of hardware (network adapters) and software (network device driver). For example, you might find Ethernet card or Fiber Distributed Data Interface (FDDI) protocols at this layer.
The second layer consists of a single protocol called Internet Protocol (IP). This is the protocol that supports the interconnection of multiple networking technologies into a single logical internetwork.
The third layer consists of two main protocols---the Transmission Control Protocol and the User Datagram Protocol (UDP). TCP and UDP provide alternative logical channels to application programs. TCP provides a bye steam channel and UDP provides an unreliable datagram service. TCP and UDP are sometimes called end to end protocol.
Running above the transport layer are a range of applicatio protocol such as FTP, TFTP, HTTP, SMTP, Telnet, etc.
Difference between application programs and application layer protocol. All the WWW browsers (Safari, Firefox, IE, Opera, Lynx, etc.) There is a similarly large numbers of webservers. The reason all of them can interwork is that they all conform to the HTTP application layer protocol.
Internet architecture does not imply strict layering. The application is free to bypass the defined transport layer protocols and to directly use IP or any of the underlying networks. In fact, programmers are free to define new channel abstractions.
Hour glass shape: Wide at the top and bottom but narrow at the waist: IP serves as the focal point of the architecture. IP is a common method of exchaning packets among a wide collection of networks.
Image source: Jennifer Ruxford

## Slide 5
Example application
Let’s assume that a student (in the gcuf.edu.pk LAN) wishes to access GCUF website hosted at www.gcuf.edu.pk
WWW
P
C
To clarify concepts, let us assume a greatly simplified model of the
LAN of GCUF
Network’s domain name: gcuf.edu.pk

## Slide 6
Example application
http://www.seecs.edu.pk
Other browsers include Firefox, Opera.
Browser acts as:
a client of webserver
fetches and displays user requested documents
1
2
This is an example of a browser (Internet Explorer)
Address Bar
Notes: The section 1.1 of chapter 1 of the textbook (P&D) has a similar example. An excerpt from the textbook follows:
The string http indicates that HTTP protocol will be used to download the page. www.seecs.edu.pk is the name of the machine that serves the page.
What most users are not aware of, however, is that by clicking on the above URL, as many as 17 messages may be exchanged (this is for the example in the book which accesses http://www.mkp.com/pd3e).
Note that www.mkp.com has three level of domains. The suffix .com is the first level domain (also called the top level domain (TLD)); other TLDs include .edu, .org, .biz, .info, etc. There are also TLDs based on the country code, e.g.: .pk, .in., ae, .au., .nz, etc. The second last domain in the example .mkp is the second level domain, and www is the third level domain. To resolve a DNS, a browser may have to go to a DNS server for each level of domain, therefore, in the example in the book, 6 messages may be exchanged (3 Request/ 3 Replies). For our example, 8 messages may be exchanged since www.seecs.edu.pk has four level of domains (therefore, 4 requests and four replies).
As we will see in our future classes, three messages are required to set up a TCP connection (this will become clear when we study the handshaking protocol used by TCP to establish connections).
Four messages for the HTTP get request and reply (request/ reply + acks for each).
Four messages are required to tear down the TCP request.
Extra messages may have to be exchanged to know the MAC address of the end machine (through the ARP protocol).

## Slide 7
Example application (contd.)
The HTTP request sent
by the student PC (the machine pc.gcuf.edu.pk)
to the webserver (the machine www.gcuf.edu.pk) would be something like “GET / HTML/1.1”
Packet so far:
Outstanding issues:
How to send this request to Webserver?
Which application at webserver must process this packet?
GET / HTML/1.1
1
2

## Slide 8
But how to send this request to Webserver?
To communicate with www.gcuf.edu.pk (hostname), its IP address must be known
How to resolve hostnames to IP addresses
Domain Name Service (DNS)
1
?
?
?
Example application (contd.)

## Slide 9
WWW
D
N
S
Example application (contd.)

## Slide 10
DNS Client/Server Exchange
WWW
D
N
S
Request
Tell me the IP address of www.gcuf.edu.pk?

## Slide 11
WWW
D
N
S
Reply
The IP address of www.gcuf.edu.pk is
DNS Client/Server Exchange

## Slide 12
Which application at webserver must process this packet?
In TCP/IP, each well-known application is identified using ports.
The port of DNS is 53; HTTP is 80; SMTP is 25.
In our considered example, HTTP server application (port 80) would process the packet.
Packet so far:
2
Source Port | Destination Port | GET / HTML/1.1
> 1024 | 80 |
Example application (contd.)

## Slide 13
The destination IP address (found through DNS)
is 202.125.157.196.
Let’s assume the source IP address is 202.125.157.150
(network must be same; to be explained later)
Packet so far:
Source IP | Destination IP | Source Port | Destination Port | GET / HTML/1.1
202.125.157.150 | 202.125.157.196 | > 1024 | 80 |
Logical addressing: network and host parts
*Assuming /24 subnet mask (to be explained later)
Example application (contd.)

## Slide 14
How to send the created packet to Webserver?
To communicate with any host, its physical address (called MAC address) must be known.
How to resolve IP addresses to MAC addresses
Address Resolution Protocol (ARP)
3
?
?
Example application (contd.)

## Slide 15
ARP Client/Server Exchange
WWW
D
N
S
Request
Any one knows the MAC (physical) address of 202.125.157.196 ?
Request

## Slide 16
WWW
D
N
S
Reply
The MAC address of 202.125.157.196 is
12:34:aa:bb:cc:dd
ARP Client/Server Exchange
The MAC address of 202.125.157.196 is 12:34:aa:bb:cc:dd

## Slide 17
Now that the physical (MAC) addresses are known, communication can take place
The destination MAC address is 12:34:aa:bb:cc:dd
The source MAC address (let’s assume) is 23:34:aa:bb:cc:dd
IP packet containing the data
MAC frame
Source IP | Destination IP | Source Port | Destination Port | GET / HTML/1.1
202.125.157.150 | 202.125.157.196 | > 1024 | 80 |
Payload
Source MAC address | Destination MAC address
FCS
Example application (contd.)

## Slide 18
Encapsulation
This topic was also covered in the last lecture
GET / HTML/1.1
Source MAC address | Destination MAC address 23:34:aa:bb:cc:dd | 12:34:aa:bb:cc:dd
FCS
Payload
Payload
Source Port | Destination Port
> 1024 | 80
Payload
Payload
Source IP | Destination IP
202.125.157.150 | 202.125.157.196
Payload
Application data
TCP Segment
MAC Frame
IP Packet

## Slide 19
HTTP Client/Server Exchange
WWW
D
N
S
Send me the index.html page for the host www.gcuf.edu.pk using HTTP version 1.1
Request

## Slide 20
WWW
D
N
S
Reply
The index.html page in the wwwroot directory configured for the www.gcuf.edu.pk webserver is sent back to the browser for display
HTTP Client/Server Exchange

## Slide 21
?
?
?
Questions/ Confusions?